## Slide 1: Turbulence Accidents and NTSB Research Update
Nathan Doble
Turbulence Impact Mitigation Workshop 3
McLean, Virginia – September 6, 2018

## Slide 2: US Civil Aviation Turbulence Accidents
Accident definition: ≥ substantial damage or ≥ serious injury
Chart: Calendar Year
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Part 121 | 6 | 14 | 10 | 16 | 12 | 5 | 6 | 12 | 13
Part 135 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 2
General Aviation | 19 | 2 | 8 | 8 | 9 | 10 | 9 | 8 | 9

## Slide 3: Defining Events Ranked by FAR Part
General Aviation |  |  |  | Part 135 |  |  |  | Part 121 |  | 
1 | Loss of Control-Inflight | 18% |  | 1 | Powerplant Malfunc | 15% |  | 1 | Turbulence | 34%
2 | Powerplant Malfunc | 18% |  | 2 | Loss of Control-Inflight | 14% |  | 2 | Ground Collision | 14%
3 | Loss of Control-Ground | 14% |  | 3 | Abnormal Rwy Contact | 12% |  | 3 | Abnormal Rwy Contact | 10%
4 | Abnormal Rwy Contact | 13% |  | 4 | Loss of Control-Ground | 9% |  | 4 | Cabin Safety Event | 9%
5 | Fuel | 5% |  | 5 | Non-Powerplant Malfunc | 8% |  | 5 | Ground Handling | 9%
⁞ | ⁞ | ⁞ |  | ⁞ | ⁞ | ⁞ |  |  |  | 
⁞ | ⁞ | ⁞ |  | 14 | Turbulence | 1% |  |  |  | 
21 | Turbulence | <1% |  |  |  |  |  |  |  | 
2008-2016 US civil aviation accidents
Defining events from 32-category CAST/ICAO taxonomy

## Slide 4: Turbulence Types in Part 121 Accidents: 2008-2016
Chart: 
| Convective | Clear Air | Terrain Induced | Wake | Unspecified
 | 36 | 23 | 4 | 2 | 15

## Slide 5: Phase of Flight for Part 121 Turbulence Accidents: 2008-2016
Chart: Phase of Flight
| Approach - IFR Final Approach | Approach - IFR Initial Approach | Approach | Enroute - Descent | Enroute - Change of Cruise Level | Enroute - Cruise | Enroute - Climb to Cruise | Enroute | Initial Climb
Percent of Accidents | 0.010638 | 0.021277 | 0.10638 | 0.34043 | 0.021277 | 0.32979 | 0.085106 | 0.074468 | 0.010638

## Slide 6: Seasonality of Part 121 Turbulence Accidents: 2008-2016
Chart: Month
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
 | 3 | 13 | 5 | 8 | 10 | 9 | 10 | 9 | 4 | 7 | 6 | 10

## Slide 7: Part 121 Turbulence Injuries and Aircraft Damage: 2008-2016
6% of accidents resulted in aircraft damage
All damage classified as minor
  Ceiling panels
  Passenger service units
Every accident resulted in at least one serious injury

## Slide 8: Part 121 Turbulence Injuries: 2008-2016
Average of 12 serious injuries per year
  78% cabin crew
  22% passengers
Accounted for 45% of all Part 121 serious injuries and fatalities
Most recent Part 121 turbulence fatality in 1997
Chart: Calendar Year
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Serious (Turbulence) | 6 | 18 | 12 | 17 | 14 | 5 | 7 | 13 | 13
Serious (Non-Turbulence) | 14 | 8 | 5 | 4 | 4 | 4 | 7 | 11 | 6
Fatal | 3 | 52 | 2 | 0 | 0 | 9 | 0 | 0 | 0

## Slide 9
Notes
  Data current as of Sep. 5, 2018
  Coding scheme changed in 2008
  Data for 2008 and later includes accidents with turbulence-related cause/factor and/or defining event
  Pre-2008 data includes accidents with turbulence-related cause/factor
Part 121 Turbulence Accidents |  |  |  |  | Part 121 All Accidents |  |  |  | 
CalendarYear | AccidentsTotal | AccidentsFatal | InjuriesFatal | InjuriesSerious | AccidentsTotal | AccidentsFatal | InjuriesFatal | InjuriesSerious | FlightHours (millions)
1983 | 5 | 0 | 0 | 4 | 23 | 4 | 15 | 13 | 7.299
1984 | 6 | 0 | 0 | 5 | 16 | 1 | 4 | 11 | 8.165
1985 | 3 | 0 | 0 | 4 | 21 | 7 | 526 | 30 | 8.710
1986 | 8 | 0 | 0 | 12 | 24 | 3 | 8 | 22 | 9.976
1987 | 7 | 0 | 0 | 8 | 33 | 5 | 232 | 46 | 10.645
1988 | 6 | 0 | 0 | 6 | 29 | 3 | 285 | 57 | 11.141
1989 | 4 | 0 | 0 | 9 | 28 | 11 | 278 | 68 | 11.275
1990 | 5 | 1 | 1 | 7 | 24 | 6 | 39 | 29 | 12.150
1991 | 6 | 0 | 0 | 7 | 26 | 4 | 62 | 26 | 11.781
1992 | 4 | 0 | 0 | 3 | 18 | 4 | 33 | 22 | 12.360
1993 | 9 | 0 | 0 | 11 | 23 | 1 | 1 | 19 | 12.706
1994 | 5 | 0 | 0 | 5 | 23 | 4 | 239 | 31 | 13.124
1995 | 10 | 0 | 0 | 13 | 36 | 3 | 168 | 25 | 13.505
1996 | 10 | 0 | 0 | 15 | 37 | 5 | 380 | 77 | 13.746
1997 | 14 | 1 | 1 | 31 | 49 | 4 | 8 | 43 | 15.838
1998 | 10 | 0 | 0 | 12 | 50 | 1 | 1 | 30 | 16.817
1999 | 12 | 0 | 0 | 12 | 51 | 2 | 12 | 67 | 17.555
2000 | 14 | 0 | 0 | 17 | 56 | 3 | 92 | 31 | 18.299
2001 | 11 | 0 | 0 | 11 | 46 | 6 | 531 | 19 | 17.814
2002 | 8 | 0 | 0 | 10 | 41 | 0 | 0 | 24 | 17.290
2003 | 17 | 0 | 0 | 20 | 54 | 2 | 22 | 31 | 17.468
2004 | 11 | 0 | 0 | 11 | 30 | 2 | 14 | 20 | 18.883
2005 | 6 | 0 | 0 | 6 | 40 | 3 | 22 | 14 | 19.390
2006 | 6 | 0 | 0 | 6 | 33 | 2 | 50 | 9 | 19.263
2007 | 10 | 0 | 0 | 11 | 28 | 1 | 1 | 16 | 19.637
2008 | 6 | 0 | 0 | 6 | 27 | 2 | 3 | 20 | 19.127
2009 | 14 | 0 | 0 | 18 | 30 | 2 | 52 | 26 | 17.627
2010 | 10 | 0 | 0 | 12 | 30 | 1 | 2 | 17 | 17.751
2011 | 16 | 0 | 0 | 17 | 33 | 0 | 0 | 21 | 17.963
2012 | 12 | 0 | 0 | 14 | 26 | 0 | 0 | 18 | 17.722
2013 | 5 | 0 | 0 | 5 | 23 | 2 | 9 | 9 | 17.718
2014 | 6 | 0 | 0 | 7 | 32 | 0 | 0 | 14 | 17.752
2015 | 12 | 0 | 0 | 13 | 29 | 0 | 0 | 24 | 17.929
2016 | 13 | 0 | 0 | 13 | 31 | 0 | 0 | 19 | 18.274

## Slide 10: NTSB Turbulence-Related Activities
Accident investigations
Workshops
2016 Forum and 2017 Special Investigation Report on PIREPs
Safety Recommendations to improve weather forecasting and dissemination of weather reports
Safety Study in progress: Preventing Turbulence-Related Injuries in Part 121 Air Carrier Operations

## Slide 11: NTSB Safety Studies
NTSB mandate includes conducting “special studies and investigations about transportation safety”
Studies are (in some ways) similar to major investigation
  Report with safety recommendations
  Public board meeting to present, discuss, and adopt report and recommendations
Address transportation safety issues from a broad, nationwide perspective
Notes: Title 49 United States Code section 1116

## Slide 12: Turbulence Study: Objectives
Summarize types and causes of turbulence
Detail safety impacts on Part 121 operations
  Accident characteristics and trends
  Injury types and mechanisms
Examine methods to reduce likelihood and consequences of turbulence encounters

## Slide 13: Turbulence Study: Areas of Inquiry
Turbulence prediction and detection technologies
Resources for planning and conducting flights
Air carrier and ATC training, policies, procedures
Outcomes of past industry efforts
Aircraft technologies

## Slide 14: Turbulence Study: Methodology
Literature review
Analysis of NTSB accident data
Analysis of external data on Part 121 turbulence encounters
Stakeholder interviews
Case studies of turbulence accidents

## Slide 15: Turbulence Study: Status
Research proposal adopted by Board on September 5, 2018
Contact: nathan.doble@ntsb.gov